## Slide 1: STS 12/13 Exercie 8 Signal-to-Noise Ratio (C/N0) in total satellite link (up and down) Ľ. Maceková

## Slide 2
C/N – Signal–to-Noise Ratio (Kvalita príjmu)
(C-Carrier-nosná, i.e. frequency of harmonic time series, which is modulated by some type of modulation, N-Noise-šum)
- it is SNR, acually, on the input of the terrestrial receiver .
C/Ν[-]= Pt [W] . Gt.Gr..b / (k.T.B)
Pt...transmitted power, Gt,Gr...gain of transmitter or receiver antennas respoctively, b – losses by free space transfer between 2 antennas
known
Ďalšie parametre systému:
C/Ν[dB]= Pt [dBW]+Gt[dΒ]+Gr[dB]+b[dB]-10logk-10logT-10logB
in dB:

## Slide 3
λ...wavelength (c/f)
R...distance (for example 36.106 m at GEO)
Example:
Calculate loss of free space transfer for GEO down link at frequency 11 GHz.
Result: -206dB
b... losses by free space transfer between 2 antennas :

## Slide 4
In communications up- and down – the total Signal-to-Noise Ratio
Quality of receiving depends on the worste quality in some partial section of link (the principle of the “weakest article of the chain”)
T ...total
U ...uplink
D ...downlink
I0 ...intereference noise
(***)

## Slide 5
Example of calculation:
Communication from Earth station to aeroplane station through satellite in the system ETS-V.
(the older experimental system for communication ground-aircraft via satellite)
Notes: GES ... gate Earth station, AES ... aircraft Earth station.
From GES to satellite (uplink):
GES EIRP .....................................................60,7 dBW
propagation loss.........................................199,4 dB (d = 37270 km, f = 6GHz)
satellite antenna gain..................................21,7 dBi
feeder loss............................................3,0 dB
uplink total C = 60,7-199,4+21,7-3,0= -120,0 dBW
N0 = 10log(kTB) = -228,6 + 10log300 + 10log1Hz= -203,8 dBHz (nie je zmienka o š.pásma, takže uvažujeme kvalitu na 1 Hz)
s (C/N0)U= -120 + 203,8 = 83, 8 dBHz
Zo satelitu na lietadlo (downlink):
sat. EIRP .........................................30,5 dBW
propagation loss...... 188,5 dB (d = 41097 km, f = 1,5 GHz)
AES antenna gain................................21,7 dBi
antenna tracking error ..............3,0 dB
feeder loss...............................3,0 dB
downlink total C = 60,7-199,4+21,7-3,0= -120,0 dBW
N0 =10log(kTB)= -228,6+10log300= -203,8 dBHz 
(C/N0)D= -147,5 + 203,8 = 56,3 dBHz continue
[1]

## Slide 6
Calculation by (***) :
The result confirms, that total quality of communication channel equals to the worst one from partial links.

## Slide 7
Literatúra:
[1] S. Ohmori, H. Wakana, S. Kawase : Mobile satellite communications, Artech House, 1998.