## Slide 1: Link Budget
STS 2013/14
Exercise 4
Ľ. Maceková
Energetická bilancia satelitnej linky

## Slide 2
Fig. Illustration of several satellite link aspects [2]
Satellite
Attenuation by precipitation
G/T EIRP
Blocking
Shielding
DEM
MOD
D/C
U/C
DIP
HPA
LNA
Acoustic
data
Multipath propagation and fading (because of reflections)
Terrestrial exchange
Mobile terrestrial station
DIP
HPA
LNA
LNA
HPA
DIP
Transponder
Frequency convertor
Antenna
Antenna,
G/T, EIRP, C/No
Propagation path
Satellite
!
Attenuation by precipitation
Antenna
Propagation path

## Slide 3
Problems:
noise
gains and losses (also gains of antennas)
blocking
attenuation by surrounding environment (shielding by vegetation, rain - in the case of Ka-band and mm-waves)
multipath broadcasting (multiple reflections) – multipath fading
reflection from sea level in the case of maritime communications
But, at first, we must familiarize with:
decibel measure of power, gain, attenuation, etc.
noise power, SNR, noise temperature

## Slide 4
D ... diameter of dish (or of reflector, or of array of radiating elements, i.e. of aperture) [m]
ηA ... effective radiated surface of antenna – depends on diraction of setting of antenna = Aef [m2]
A ... aperture (physical surface, passed by e-m radiation) [m2]
η ... efficiency of aperture (0,35-0,75) [-]
λ ... wavelength [m]
- actual gain is always < than value declared by producer (connection, direction and other unfavourable conditions)
GdBi = 10 log G [dBi]
Example: η=55%, f=11GHz, D=1m. G=?
Gain of parabolic antenna in dependence on both dish diameter an efficiency:
Antenna gain – in dependence on generalized aperture and referenced to gain of isotropic radiator :
Example: Calculate λ of frequency channel at 900 MHz.
Results: about 7299 and 38dBi
... in comparison with isotropic antenna

## Slide 5
5
…… > 0 dB
= 10log(P2 /1mW) – 10 log( P1 /1mW )
G[dB] = P 2 [dBm] – P 1 [dBm]
[W alebo mW]
P[dBW]=10logP[W]
P[dBm]=10logP[mW]
- if we transform:
and by definition of dBm:
Decibels
P1
P2
 Gain 
If P2 > P1
Definition of dBm and dBW
Then – similarly: attenuation, diminution, Loss
P1 > P2; L > 0 dB

G
(L)
device or signal path

## Slide 6
Examples ...
1 W  ? dBW
1mW  ? dBW
1mW  ? dBm
10 mW  ? dBm
35 mW  ? dBm
P1 = 1mW, P2 = 10 W, A = ? (A… Attenuation)
P = 35 dBm  ? mW
P = - 15 dBW  ? W

## Slide 7
Other parameters of satellite receiving

## Slide 8
Noise
(Šum)

## Slide 9
Noise, Signal-to-Noise Ratio SNR (S/N in [-]) and Signal-to-Noise Ratio in [dB] , Noise Figure F (or NF), noise voltage, noise power, Power Spectral Density of noise (PSDN), ...
Effective noise voltage (by Nyquist [2])
k – Boltzmann konstant = 1,38. 10-23Ws-1K-1
T – absolut. temperature [K]
R – equiv. resistivity [Ω]
B – frequency bandwidth [Hz]
S/N ... ratio [W,W; result is without units]
SNRdB = 10 log (S/N) [dB] = SdBm – NdBm [dB]
(S/N)in, (S/N)out, SNRin, SNRout
Signal-to-Noise Ration in non units and in dB
S ... signal power
N ... noise power (šum=noise)
SNR ... signal-to-noise ratio

## Slide 10
Power of noise (if matched connecting : Rsource=RLoad =R)
 density of energy N0 – power spectral density of noise (power over unit of freq. spectrum, i.e. over 1 Hz):
[W/Hz]
if in [dB], so as follows:
[dBW/Hz]
[dBW/Hz]
Example: Evaluate density of noise energy of resistor at temperature 27°C
Result: -203,8 dBW/Hz
...symbolic notation for dB-calculi

## Slide 11
Noise Figure (F) of device with gain G
We know:
S/N ... ratio [-]
SNRdB = 10 log (S/N) [dB]
(S/N)in, (S/N)out, SNRin, SNRout 
where:
Te ...equivalent noise temperature of el. device at the input
T0 ...operational (circumstances) physical temperature
F = 10 log F = SNRin[dB] – SNRout[dB] [dB]
[without units]
Noise figure NF, alebo len F – šumové číslo aktívneho zariadenia (zosilňovača, antény atď.)
Sin,Nin,
SNRin
G...Gain
F
Sout,Nout,
SNRout
Sout = G . Sin
Nout=G.Nin+Nown
And then in dB:
Noise is property of every substance  each el. amplifier, beyond amplifying of entering signal and noise, adds its own noise, as well.  important parameter of active el. equipments (antennas, amplifiers, :

## Slide 12
Example 1: Evaluate the noise figure of amplifier at circumstances temperature T0 = 300 K and at Tin = 400 K.
Result: 3,7 dB
Example 2: Calculate the equivalent input noise temperature of amplifier, if we know the circumstances temperature To = 290 K, and noise figure NF= 4 dB.
Result: Te = 438,8 K

## Slide 13
Noise Figure (FL) of device with insert loss L (attenuation) – feed lines, cables, connectors, etc.
Te ...equivalent noise temperature at the input
T0 ...operational (circumstances) temperature
Tout ... Output noise temperature
FL[dB] = 10 log FL [dB]
[without units]
noise figure FL – šumové číslo zariadenia:
Sin,Nin,
SNRin
L ... Loss
FL
Sout,Nout,
SNRout
L > 1
 Sout = Sin/L; Sout<Sin
Then in dB:
Then input noise temperature:
And output noise temperature.:


## Slide 14
Example - both input and output noise temperatures of loss device:
Circuit has loss 2,5 dB, operational temperature is 400 K. Evaluate equivalent noise temperature at both his input and output ports.
Results: Te = 311,3 K, Tout=175,1 K
Outcome:
Circuit with loss decrements equivalent noise temperature – suppresses noise! 

## Slide 15
G1
G2
L1
L2
Ga, Ta
P1
Overall equivalent noise temperature of the complete cascade (converted into the point P1; not yet with antenna):
 It depends almost on noise properties of first stages (for examples antenna feed L1 and input amplifier G1) !! (all G are >> 1)
That is, why requirement of LNA – Low Noise Amplifier – of receiver is important and crucial (our aim is: as best / as high SNR as possible !!).
or LNC – Low Noise Convertor

## Slide 16
Total noise temperature of system Ts at the input of receiver with antenna:
or :
T=Ta.a + (1-a)T0+(F-1)T0
where:
TR ... noise temperature of the first amplifier stage of receiver (Low Noise Amplifier - LNA); TR = (F-1).T0
Lf ... loss of feed line (between antenna and LNA); LF=1/a ... about 1/ 0,95
Ta... noise temperature at output of antenna (about 80 K to 100K in L-band)
(*)
... with considering of antenna:

## Slide 17
Gain of antenna and EIRP (Effective Isotropic Radiated Power)
Ga [dBi]= 10 log (Φ/ Φi) ... [dBi]
Φi = Pt / 4πR2 ...
(We know, what are: isotropic antenna, directional antenna, beam width- at -3dB
level of maximal power of signal)
Φi ... density of radiated power of isotropic antenna(or PFD- Power Flux Density) [W/m2]
Pt... radiated power [W]
R .... distance between transmitting and receiving antennas [m]
  = its radiation effectivity in comparison with reference antenna, e.g. isotropic one (that means: the gain is the result of the ratio of 2 power densities!) :
Note: PFD on the Earth surface (of the signal from satellite transmitter) – falls with horizontal distance from nadir (nadir or boresight – zamierenie - the point “under” the satellite; it relates with directional characteristic of antenna ...)
Ga = Φ / Φi
Gain of directional antenna Ga
... note.: G of isotrop. antenna is 1 (i.e. 0 dBi)

## Slide 18
EIRP = Pt .Gt [-] [W; W, -] EIRP= Pt . Gt = Pt . (Φt/ Φi) = ... = Φt. 4πR2
or, in dB:
EIRP[dBW] = 10 log Pvys [W] + Gvys [dBi]
Example:
If EIRP of transmitter in GEO system is 48 dBW, calculate the maximal PFD on the Earth.
Pt … radiated power (of transmitter) [W]
Gt ... gain of transmitting antenna (on the sat.)
EIRP ... Equivalent Isotropic Radiated Power of satellite transmitter
result: -114 dBW/m2

## Slide 19
G/T - Figure of merit (Systémový zisk)
the ratio of the gain and noise temperature of equipment - important parameter – higher the better
G/T of antennas mostly contains also noise temperature of convertor
The next parameters of system:
Example:
Evaluate figure of merit of antenna with LNC-convertor. Noise figure of LNC is F=1,3, gain of antenna at mean frequency 12,1GHz is 34,75 dBi, its noise temperature is 31,68K, loss between radiator and convertor is about a=0,95, loss because of inaccurate bearing and polarization setting is about b=0,9. Consider reference operational temperature T0=290K.
Solution:
We use equation (*) for equivalent noise temperature of system of antenna with convertor:
T=Ta.a + (1-a)T0+(F-1)T0; and for operational gain of antenna Gp=a.b.G[-].  then Gp/T=…
Result: 17,7 K-1... 12,48 dB/K

## Slide 20
C/N – Kvalita príjmu
(C-Carrier-nosná,t.j. nosná frekvencia signálu, N-Noise-šum)
- je to vlastne pomer signálu a šumu na vstupe pozemného prijímača – čiže to, čo sme predtým nazvali SNR .
C/Ν[-]= Pt [W] . Gt.Gr..b / (k.T.B)
Pt...vyslaný výkon, Gt,Gr...zisk vysielacej, resp. prij. antény, b-útlm voľ.priestoru medzi anténami
pozri ďalej
Ďalšie parametre systému:
Quality of receiving signal - Signal-to-Noise Ratio in Satellite Communication
C/Ν[dB]= Pt [dBW]+Gt[dΒ]+Gr[dB]+b[dB]-10logk-10logT-10logB
in dB:
When noise power density is C/N0 is considered, we can write:

## Slide 21
λ...vln.dĺžka
R...vzdialenosť (napr. 36.106 m pre GEO)
Príklad:
Vypočítať útlm pre systém GEO pri frekvencii 11 GHz.
Výsledok: -206dB
b...útlm voľného priestoru od vysielacej antény ku prijímacej:

## Slide 22: Takže teraz ten rozpočet linky
Vysielanie:
+ Výkon HPA
Vysielacie straty
(káble a konektory)
+ Zisk antény
EIRP
Tx
Strata zameraním antény Tx
Strata vo voľnom priesore
Atmosferické straty (plyny, mraky, dážď)
- Strata zameraním antény Rx
Rx
Príjem
+ Zisk antény
Prijímacie straty
(káble a konektory)
+ Príspevok šumovej teploty
Pr
všetky faktory sa započítajú
ako prírastky (+) alebo
mínusy (-) v [dB]
(viď obr. na 2. slide)
zdroj [1]
(Link Power Budget)

## Slide 23
Zdroje:
[1] J. Montana: Introduction to Satellite Communications, George Mason Univ. 2003
[2] Mobilné satelitné komunikácie